24/10/17
- Started looking at motors which will turn the sides of the cube (https://www.aliexpress.com/item/DC-6V-12V-50-300RPM-Gear-Motor-Speed-Reduction-Gear-DC-Motor-Electric-Gear-Box-with/32821679631.html?spm=2114.search0204.0.0.NZDYjp)
- Started desigining the core of the cube using OpenSCAD

27/10/17
Started thinking about and discussing design features / specifications for our 3d printer (which we will use to print the cube).
03/11/17
Decided that the cube will have removable tiles on each face and started working on the design for this.
07/11/17, 10/11/17
- Designed the tile and cut out the tile pieces from the centres, edges and corner pieces so we can print them separately (and coloured) to fit into the cube pieces.
- Also scaled up all the pieces so that they are the right size for our cube – our cube will wil be 300mm in each direction (about five times larger than a standard cube)

14/11/17
Exported the cube pieces so they can be 3d printed – hopefully we will have some on Friday (17/11).
10/04/18
Decdied we will be using stepper motors with encoders to turn each side. NEMA 11 size means that each side of the motor is 1.1 inches which we think will be a good size. We also calculated we will need a minimum of 3.75 rpm, which is easy to make happen. We need to do some scale drawings (maybe on solvespace) to show size and shape of the motors and how they will fit in the core.
17/04/18
- Changed 3d code so that the plastic is much thinner and there is more space for the motors and other components
- Put each piece into its own file for ease of printing
- Changed the core piece so that the six tunnels extending from each side are square, meaning that the motors will fit perfectly.
23/04/18
Changed the OpenSCAD files to make each individual piece hollow. This will make it much faster to print and make the whole cube lighter as well.